## Slide 1: Button Input: On/off state change
Living with the Lab
Gerald Recktenwald
Portland State University
gerry@pdx.edu

## Slide 2: User input features of the fan
Potentiometer for speed control
  Continually variable input makes sense for speed control
  Previously discussed
Start/stop
  Could use a conventional power switch
  Push button (momentary) switch
Lock or limit rotation angle
  Button click to hold/release fan in one position
  Potentiometer to set range limit

## Slide 3: Conventional on/off switch
Basic light switch or rocker switch
  Makes or breaks connection to power
  Switch stays in position: On or Off
  Toggle position indicates the state
  NOT in the Arduino Inventors Kit
Image from lowes.com
Image from sparkfun.com

## Slide 4: How does a button work?
Simple switch schematic
Use DMM to measure open/closed circuit
Map the pin states

## Slide 5: Measure Open and Closed Circuits
 | Measured Resistance (Ω) | 
Connect Pins | When not pressed | When pressed
1 and 2 |  | 
1 and 3 |  | 
1 and 4 |  | 
2 and 3 |  | 

## Slide 6: Measure Open and Closed Circuits
 | Measured Resistance (Ω) | 
Connect Pins | When not pressed | When pressed
1 and 2 |  | 
1 and 3 |  | 
1 and 4 |  | 
2 and 3 |  | 
Sketch Connections:
Data from Measurements:

## Slide 7: Push Button Switches
A momentary button is a “Biased Switch”
Pushing the button changes state
State is reversed (return to biased position) when button is released
Two types
  NO: normally open
  NC: normally closed

## Slide 8: Momentary or push-button switches
Normally open
  electrical contact is made when button is pressed
Normally closed
  electrical contact is broken when button is pressed
Internal spring returns button to its un-pressed state
Image from sparkfun.com

## Slide 9: Putting buttons into action
Build the circuit: same one is used for all examples
  Test with LED on/off
  LED is only controlled by the button, not by Arduino code
Create a “wait to start” button
  Simplest button implementation
  Execution is blocked while waiting for a button click
Use an interrupt handler
  Most sophisticated: Don’t block execution while waiting for button input
  Most sophisticated: Requires good understanding of coding
  Requires “de-bouncing”
  Not too hard to use as a black box

## Slide 10: Momentary Button and LED Circuit
Digital input with a pull-down resistor
  When switch is open (button not pressed):
    Digital input pin is tied to ground
    No current flows, so there is no voltage difference from input pin to ground
    Reading on digital input is LOW
  When switch is closed (button is pressed):
    Current flows from 5V to ground, causing LED to light up.
    The 10k resistor limits the current draw by the input pin.
    The 330Ω resistor causes a large voltage drop between 5V and ground, which causes the digital input pin to be closer to 5V.
    Reading on digital input is HIGH

## Slide 11: Technical Note
Usually we do not include an LED directly in the button circuit. The following diagrams show plan button circuits with pull-up and pull-down resistors. In these applications, the pull-up or pull-down resistors should be 10k. Refer to Lady Ada Tutorial #5:
  http://www.ladyada.net/learn/arduino/lesson5.html
Pull-up
resistor:
Pull-down
resistor:

## Slide 12: Programs for the LED/Button Circuit
Continuous monitor of button state
  Program is completely occupied by monitoring the button
  Used as a demonstration — not practically useful
Wait for button input
Interrupt Handler
All three programs use the same electrical circuit

## Slide 13: Continuous monitor of button state
int button_pin = 4; // pin used to read the button
void setup() {
pinMode( button_pin, INPUT);
Serial.begin(9600); // Button state is sent to host
}
void loop() {
int button;
button = digitalRead( button_pin );
if ( button == HIGH ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
Serial monitor shows a continuous stream of “on” or “off”
This program does not control the LED

## Slide 14: Programs for the LED/Button Circuit
Continuous monitor of button state
  Program is completely occupied by monitoring the button
  Used as a demonstration — not practically useful
Wait for button input
  Blocks execution while waiting
  May be useful as a start button
Interrupt Handler
All three programs use the same electrical circuit

## Slide 15: Wait for button input
int button_pin = 4; // pin used to read the button
void setup() {
int start_click = LOW; // Initial state: no click yet
pinMode( button_pin, INPUT);
Serial.begin(9600);
while ( !start_click ) {
start_click = digitalRead( button_pin );
Serial.println("Waiting for button press");
}
}
void loop() {
int button;
button = digitalRead( button_pin );
if ( button == HIGH ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
Same loop() function as in the preceding sketch
while loop continues as long as start_click is FALSE

## Slide 16: Programs for the LED/Button Circuit
Continuous monitor of button state
  Program is completely occupied by monitoring the button
  Used as a demonstration — not practically useful
Wait for button input
  Blocks execution while waiting
  May be useful as a start button
Interrupt Handler
  Most versatile
  Does not block execution
  Interrupt is used to change a flag that indicates state
  Regular code in loop function checks the sate of the flag
All three programs use the same electrical circuit

## Slide 17: Interrupt handler for button input
int button_interrupt = 0; // Interrupt 0 is on pin 2 !!
int toggle_on = false; // Button click switches state
void setup() {
Serial.begin(9600);
attachInterrupt( button_interrupt, handle_click, RISING); // Register handler
}
void loop() {
if ( toggle_on ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
void handle_click() {
static unsigned long last_interrupt_time = 0; // Zero only at start
unsigned long interrupt_time = millis(); // Read the clock
if ( interrupt_time - last_interrupt_time > 200 ) { // Ignore when < 200 msec
toggle_on = !toggle_on;
}
last_interrupt_time = interrupt_time;
}

## Slide 18: Interrupt handler for button input
int button_interrupt = 0; // Interrupt 0 is on pin 2 !!
int toggle_on = false; // Button click switches state
void setup() {
Serial.begin(9600);
attachInterrupt( button_interrupt, handle_click, RISING); // Register handler
}
void loop() {
if ( toggle_on ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
void handle_click() {
static unsigned long last_interrupt_time = 0; // Zero only at start
unsigned long interrupt_time = millis(); // Read the clock
if ( interrupt_time - last_interrupt_time > 200 ) { // Ignore when < 200 msec
toggle_on = !toggle_on;
}
last_interrupt_time = interrupt_time;
}
Interrupt handler must be registered when program starts
The interrupt handler, handle_click, is a user-written function that is called when an interrupt is detected
button_interrupt is the ID or number of the interrupt. It must be 0 or 1
A RISING interrupt occurs when the pin changes from LOW to HIGH

## Slide 19: Interrupt handler for button input
int button_interrupt = 0; // Interrupt 0 is on pin 2 !!
int toggle_on = false; // Button click switches state
void setup() {
Serial.begin(9600);
attachInterrupt( button_interrupt, handle_click, RISING); // Register handler
}
void loop() {
if ( toggle_on ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
void handle_click() {
static unsigned long last_interrupt_time = 0; // Zero only at start
unsigned long interrupt_time = millis(); // Read the clock
if ( interrupt_time - last_interrupt_time > 200 ) { // Ignore when < 200 msec
toggle_on = !toggle_on;
}
last_interrupt_time = interrupt_time;
}
toggle_on is a global variable that remembers the “state”. It is either true or false (1 or 0).
The loop() function only checks the state of toggle_on. The value of toggle_on is set in the interrupt handler, handle_click.
The value of toggle_on is flipped only when a true interrupt even occurs. De-bouncing is described in the next slide.

## Slide 20: Interrupt handler for button input
int button_interrupt = 0; // Interrupt 0 is on pin 2 !!
int toggle_on = false; // Button click switches state
void setup() {
Serial.begin(9600);
attachInterrupt( button_interrupt, handle_click, RISING); // Register handler
}
void loop() {
if ( toggle_on ) {
Serial.println("on");
} else {
Serial.println("off");
}
}
void handle_click() {
static unsigned long last_interrupt_time = 0; // Zero only at start
unsigned long interrupt_time = millis(); // Read the clock
if ( interrupt_time - last_interrupt_time > 200 ) { // Ignore when < 200 msec
toggle_on = !toggle_on;
}
last_interrupt_time = interrupt_time;
}
Value of a static variable is always retained
Ignore events that occur in less than 200 msec from each other. These are likely to be mechanical bounces.
Use long: the time value in milliseconds can become large
Clock time when current interrupt occurs
Save current time as the new “last” time

## Slide 21: Other references
Ladyada tutorial
  Excellent and detailed
  http://www.ladyada.net/learn/arduino/lesson5.html
Arduino reference
  Minimal explanation
    http://www.arduino.cc/en/Tutorial/Button
  Using interrupts
    http://www.uchobby.com/index.php/2007/11/24/arduino-interrupts/
    http://www.arduino.cc/en/Reference/AttachInterrupt