## Slide 1: Basic DC Motor Circuits
Living with the Lab
Gerald Recktenwald
Portland State University
gerry@pdx.edu

## Slide 2: DC Motor Learning Objectives
Explain the role of a snubber diode
Describe how PWM controls DC motor speed
Implement a transistor circuit and Arduino program for PWM control of the DC motor
Use a potentiometer as input to a program that controls fan speed

## Slide 3
What is a snubber diode
and why should I care?

## Slide 4: Simplest DC Motor Circuit
Connect the motor to a DC power supply
Switch open
Switch closed

## Slide 5: Current continues after switch is opened
Opening the switch does not immediately stop current in the motor windings.

## Slide 6: Reverse current
Charge build-up can cause damage

## Slide 7: Motor Model
Simple model of a DC motor:
  Windings have inductance and resistance
  Inductor stores electrical energy in the windings
  We need to provide a way to safely dissipate electrical energy when the switch is opened

## Slide 8: Flyback diode or snubber diode
Adding a diode in parallel with the motor provides a path for dissipation of stored energy when the switch is opened

## Slide 9
Pulse-width modulation (PWM)
for DC motor speed control

## Slide 10: Controlling DC Motor Speed
The voltage supplied to a DC motor controls its speed
Arduino cannot supply variable DC output
  Arduino lacks a true analog output
  Use Pulse-width modulation (PWM) to simulate a variable DC supply voltage
  PWM is a common technique for supplying variable power levels to “slow” electrical devices such as resistive loads, LEDs, and DC motors
  Arduino Uno has 6 PWM pins: Digital I/O pins 3, 5, 6, 9,10, and 11

## Slide 11: Arduno Uno has 6 PWM pins
Look for the ~ prefix on the digital pin label, e.g. ~3

## Slide 12: PWM: Pulsed with modulation
PWM simulates DC voltage control for slow loads
The effective voltage is
is called the duty cycle

## Slide 13: Arduino PWM commands
Configure the output pin:
Set the duty cycle
The duty cycle is an 8 bit value:
0 ≤ duty_cycle ≤255
PWM_pin = ... ; // one of 3, 5, 6, 9, 10, 11
void setup() {
pinMode( PWM_pin, OUTPUT);
}
void loop() {
int duty_cycle = 150; // between 0 and 255
analogWrite( PWM_pin, duty_cycle );
}

## Slide 14
Using a transistor to switch the load

## Slide 15: Transistor as the switching device
Each Arduino output channels has a 40 mA limit
The maximum current draw for an Arduino is 200 mA
Use Arduino as the brain
Let another switching element be the brawn

## Slide 16: Use an NPN Transistor as a switch
This device is designed for use as a medium power amplifier and switch requiring collector currents up to 500 mA

## Slide 17: Electronic components in the fan kit
Transistor
Diode
220 Ω or 330 Ω
resistor

## Slide 18: Replace the Switch with a Transistor
A transistor allows on/off control to be automated and it allows switching of more current than an Arduino digital pin can supply.
Pin 9 or another PWM pin drives the transistor base

## Slide 19: Alternative locations for the transistor
Moving the transistor (and any switch) between the power supply and the motor adds a bit of safety by tying the motor to ground when the system is idle

## Slide 20: Diode and transistor orientation

## Slide 21: Arduno Uno has 5 PWM pins
Look for the ~ prefix on the digital pin label, e.g. ~3

## Slide 22: DC Motor Circuit on tiny breadboard

## Slide 23: +5V connections

## Slide 24: PWM signal is connected to transistor base

## Slide 25: Arduino program to spin the DC Motor
// spin_DC_motor.ino Use PWM to control DC motor speed
int motorPin = 3; // Pin 3 has PWM, connected it to the DC motor
void setup() {
pinMode(motorPin, OUTPUT); // Set motor pin to output mode
}
void loop() {
analogWrite(motorPin, 150); // Motor at 150/255 of full speed
delay(1000);
analogWrite(motorPin, 250); // Motor at 250/255 of full speed
delay(1000);
}
Code is in spin_DC_motor.ino

## Slide 26
User input to control fan speed

## Slide 27: Adjust fan speed with potentiometer input
Use the potentiometer circuit from the earlier analog input exercise

## Slide 28: Adjust fan speed with potentiometer input
// File: DC_motor_speed_control.pde
//
// Use potentiometer input to set the speed of a DC motor
// Output to the motor is PWM
int motorPin = 3; // pin connected to the DC motor
int potPin = 1; // analog input connected to the potentiometer
void setup()
{
pinMode(motorPin, OUTPUT);
}
void loop()
{
int PWMoutput, potReading;
potReading = analogRead(potPin);
PWMoutput = map(potReading, 0, 1023, 0, 255 );
analogWrite(motorPin, PWMoutput);
}
Code is in DC_motor_speed_control.ino

## Slide 29: Adjust fan speed with potentiometer input
Each time through the loop:
  Read the voltage at the potentiometer wiper
    Input value is a 10-bit integer: 0 ≤ potReading ≤ 1023
  Scale the 10-bit value (max 1023) to an 8-bit value (max 255)
    PWMoutput = map( potReading, 0, 1023, 0, 255 );
  Update the PWM signal
    analogWrite(motorPin, PWMoutput);
void loop() {
int PWMoutput, potReading;
potReading = analogRead(potPin);
PWMoutput = map(potReading, 0, 1023, 0, 255 );
analogWrite(motorPin, PWMoutput);
}
range for
potReading
range for
PWMoutput